| Slow Flight > 4,000 ft. MSL Clearing turns Boost pumps -----Off Cowl flaps ---------Open Gas ----------------- Mains Undercarriage ----Down Flaps ---------------- Full Mixture ------------- Best Power Power Set -------- 15” @ Full rpm Airspeed ---------- 70 kts Departure Stall > 4,000 ft. MSL Clearing turns Airspeed ----------Slow to Blue Line Boost pumps -----Off Cowl flaps ---------Monitor Gas ----------------- Mains Undercarriage ----Down Mixture ------------- Best Power Power Set -------- 21” @ Full rpm Pitch up 200 to stall buffet Recovery – Full throttle Flaps up Gear up Poff Stall > 4,000 ft. MSL Clearing turns Boost pumps -----Off Cowl flaps ---------Monitor Gas ----------------- Mains Undercarriage ----Down Mixture ------------- Best Power Power Set -------- 15” @ 2300 Flaps --------------- Extend Airspeed ----------- 90 kts Recovery – Full throttle Flaps up Gear up | Vmc Demo 6,000 ft. MSL Clearing turns Boost pumps -----Off Cowl flaps ---------Closed dead engine Open good engine Gas ------------------ Mains Undercarriage -----Up Mixture -------------- Best Power Power/Props------- Full on both Left engine --------- Close throttle Right engine ------- Full Power Pitch ----------------- 100 kts. Bank ----------------- 00 bank Increase pitch ----- 1 kt./sec. to Vmc Recover at: Loss of directional control Full rudder Stall horm/buffet Recovery: Reduce power good engine Lower nose Pitch for blue line Restore full power to inop. engine Accelerated Stall > 4,000 ft. MSL Clearing turns Boost pumps -----Off Cowl flaps ---------Monitor Gas ----------------- Mains Undercarriage ---- Down Mixture ------------- Best Power Power--------------- 16” Full RPM Airspeed ----------- 100 kts (blue line) Bank ---------------- 450 Add backpressure to buffet Recovery: Full throttle Flaps up Gear up | Steep Turns Clearing turns Boost pumps -----Off Cowl flaps ---------Closed Gas ----------------- Either tanks Undercarriage ----Up Mixture ------------- Best Power Power Set -------- 17” @ 2300 Airspeed ------- < 140 kts Bank -------------- >500 Add 3” MP in turn Emergency Descent Clearing turns Boost pumps -----Off Cowl flaps ---------Closed Gas ----------------- Mains Undercarriage ----Down Mixture ------------- Best Power Power --------------- OFF Props---------------- Full RPM at Blue line Bank ---------------- 45 degrees Airspeed -------- 140 kts 130 pitch down Start recovery at 4,300 MSL Recover before 4,000 MSL Gear up Restore power to cruise Short Field Takeoff Flaps ---------- 100 Brakes -------- Hold Power – 2,000 RPM – check guages Power –------- Full Rotate -------- 80 kts/redline Vx -------------– 84 to 50 ft. Pitch ------------130 then 100 pitch Flaps/Gear---- Retract Vy 101 kts | Short Field Landing Flaps ------------- Full Airspeed -------- 85-90 Kts T/D --------------- +100 ft. Engine Fire In-Flight Shut-Down Fuel selector ----------------Off Throttle -----------------------Close Prop -------------------------- Feather Mixture ------------------------Idle Cut-off Aux fuel pump -------------- Off Gen./ Mags. ----------------- Off Gear --------------------------- Down Airspeed ---------------------- 143 Air Start/Un-Feathering 1. Mixture--------------------------- Rich 2. Throttle -------------------------- Full 3. Boost Pump --------------- High then off 4. Throttle --------------------------- Off idle 6. Move Prop Control Out of Feather 7. When engine starts, move throttle to 15” and 2,000 RPM to warm engine Manual Gear Extension Reduce airspeed to 100-120 ks Pull landing gear motor circuit breaker Lower landing gear lever Hand crank counterclockwise Check all Down indicators Verify gear lights and horn Drag Demonstration Clearing turns Boost pumps -----Off Cowl flaps ---------Monitor Gas ----------------- Either Mixture ------------- Best Power Power---------------16” Full RPM 11” Left Airspeed -----------100 kts (blue line) Flaps --------------- 100 at a time Gear ---------------- Extend Flaps ---------------- Retract Throttle -------------- Idle |
| --- | --- | --- | --- |